## Slide 1: Design of a CPU FPGA-Based in Verilog

## Slide 2: Whoa!
This can be the part of the presentation where you introduce yourself, write your email…

## Slide 3: Table of contents 01 03 02 04
Introduction
Design
Motivation
Architecture
05
Ending
06
Microcontroller and FPGA

## Slide 4: Introduction 01
You can enter a subtitle here if you need it

## Slide 5: Manufacturing process
We opt for FPGAs due to their cost-effectiveness and open-source accessibility, aligning with our commitment to efficiency and community-driven development.

## Slide 6: Microprocessor
A microprocessor is the central processing unit (CPU) of a computer or microcontroller, responsible for executing instructions, performing arithmetic and logic operations, and managing data flow within electronic devices.

## Slide 7: What to excpect in the future
Assymbly code design
Compilers design
Serial comminication design
Debugger design
Application or game demo

## Slide 8: Personality type career
Using HDL
Elementary logic gates
16-bit variants
Multi-way variants Or
Week 01
Using Verilog
Elementary logic gates
16-bit variants
Multi-way variants Or
Week 02
Building ALU using Verilog and HDL
Week 03
Building a Bit, Register and Pc counter using Verilog and HDL.
Week 04
Building ROM, RAM and Memory using Verilog .
Week 06
Building CPU using Verilog.
week 05

## Slide 9: Awesome words

## Slide 10: —Someone Famous
“This is a quote, words full of wisdom that someone important said and can make the reader get inspired”

## Slide 11: Architecture 3

## Slide 12: Computer System

## Slide 13: Computer system
A microprocessor system consists of data input, storage, processing and output devices, under the control of a CPU.

## Slide 14: The Hack Computer
A 16-bit machine consisting of the following elements:
Both memory chips are 16-bit wide and have 15-bit address space.

## Slide 15: The Hack Computer
A 16-bit machine consisting of the following elements:
-Data memory : RAM – an addressable sequence of registers
-Instruction memory : ROM – an addressable sequence of registers
-Registers : D, A, M, where M stands for RAM[A]
-Processing : ALU, capable of computing various functions
-Program counter : PC, holding an address
-Control : The ROM is loaded with a sequence of 16-bit instructions, one per memory location, beginning at address 0.
-Instruction set : Two instructions: A-instruction, C-instruction.

## Slide 16: The A-Instruction
Used for :
Entering a constant value ( A = value)
Selecting a RAM location ( register = RAM[A])
Selecting a ROM location ( PC = A )
@17 // A = 17
D = A // D = 17
Coding example :
@17 // A = 17
D = M // D = RAM[17]
M = -1 // RAM[17]=-1
@17 // A = 17
JMP // fetch the instruction
// stored in ROM[17]

## Slide 17: The C-Instruction
Used for :
Entering a constant value ( A = value)
Selecting a RAM location ( register = RAM[A])
Selecting a ROM location ( PC = A )
@17 // A = 17
D = A // D = 17
Coding example :
@17 // A = 17
D = M // D = RAM[17]
M = -1 // RAM[17]=-1
@17 // A = 17
JMP // fetch the instruction
// stored in ROM[17]

## Slide 18: CPU

## Slide 19: ALU

## Slide 20: The Hack ALU
if (out == 0) then zr = 1, else zr = 0
if (out < 0) then ng = 1, else ng = 0
These two control bits will come into play when we build the complete computer’s architecture.

## Slide 21: Design 4

## Slide 22: PC

## Slide 23: Bit - Register
Bit Verilog
module Bit( input clk, input in, input load, output out ); wire w1,w2; Mux m1(w2,in,load,w1); DFF d1(.clk(clk),.in(w1),.out(w2)); assign out=w2; Endmodule

## Slide 24: The Hack ALU
if (out == 0) then zr = 1, else zr = 0
if (out < 0) then ng = 1, else ng = 0
These two control bits will come into play when we build the complete computer’s architecture.

## Slide 25: Bit - Register
Register HDL
CHIP Register { IN in[16], load; OUT out[16]; PARTS: Bit(in=in[0],load=load,out=out[0]); Bit(in=in[1],load=load,out=out[1]); Bit(in=in[2],load=load,out=out[2]); Bit(in=in[3],load=load,out=out[3]); Bit(in=in[4],load=load,out=out[4]); Bit(in=in[5],load=load,out=out[5]); Bit(in=in[6],load=load,out=out[6]); Bit(in=in[7],load=load,out=out[7]); Bit(in=in[8],load=load,out=out[8]); Bit(in=in[9],load=load,out=out[9]); Bit(in=in[10],load=load,out=out[10]); Bit(in=in[11],load=load,out=out[11]); Bit(in=in[12],load=load,out=out[12]); Bit(in=in[13],load=load,out=out[13]); Bit(in=in[14],load=load,out=out[14]); Bit(in=in[15],load=load,out=out[15]); }

## Slide 26: Elementary logic gates
Basic gates build using universal NAND gate

## Slide 27: NOT Gate
We build NOT gate by connecting both inputs of NAND gate to the input signal.
NOT
CHIP Not { IN in; OUT out; PARTS: Nand(a=in,b=in,out=out); }

## Slide 28: AND Gate
We build an AND gate by connecting the two inputs A and B to a NAND gate and then connecting the result to both inputs of the NAND gate.
AND
CHIP And { IN a, b; OUT out; PARTS: Nand(a=a,b=b,out=w1); Nand(a=w1,b=w1,out=out); }

## Slide 29: OR Gate
We build an OR gate by taking the NAND of two NAND gates where each input is connected to the same input signal (A or B).
OR
CHIP Or { IN a, b; OUT out; PARTS: Nand (a=a,b=a,out=w1); Nand (a=b,b= b, out=w2); Nand(a=w1,b=w2,out=out); }

## Slide 30: XOR Gate
We build an XOR gate by using NAND gates to construct the inputs and intermediate signals so that the final NAND operation produces an XOR gate.
XOR
CHIP Xor { IN a, b; OUT out; PARTS: Nand(a=a,b=a,out=w1); Nand(a=b,b=b,out=w2); Nand(a=w1,b=b,out=3); Nand(a=w2,b=a,out=4); Nand(a=w3,b=w4,out=out); }

## Slide 31: MUX Gate
We build a MUX using 4 NAND gates. We connect A to an inverted selection line, B to a non-inverted selection line, and then combine the results using another NAND gate.
MUX HDL
CHIP Mux { IN a, b, sel; OUT out; PARTS: Nand(a=sel,b=b,out=w1); Nand(a=sel,b=sel,out=w2); Nand(a=w2,b=a,out=w3); Nand(a=w1,b=w3,out=out); }

## Slide 32: MUX Gate
We build a MUX using 4 NAND gates. We connect A to an inverted selection line, B to a non-inverted selection line, and then combine the results using another NAND gate.
MUX Verilog
module Mux( input a, input b, input sel, output out ); wire w1,w2,w3; nand Nand1(w1,sel,b); nand Nan2(w2,sel,sel); nand Nan3(w3,a,w2); nand Nand4(out,w1,w3); Endmodule

## Slide 33: DMUX Gate
We build a DMUX using 5 NAND gates. We connect the input to one NAND gate with an inverted selecting line, and another NAND gate with a non-inverted selecting line. At the final stage, we connect each result to an inverter NAND gate.
DMUX HDL
CHIP DMux { IN in, sel; OUT a, b; PARTS: Nand(a=sel,b=sel,out=w1); Nand(a=in,b=w1,out=w2); Nand(a=in,b=sel,out=w3); Nand(a=w2,b=w2,out=a); Nand(a=w3,b=w3,out=b); }

## Slide 34: DMUX Gate
We build a DMUX using 5 NAND gates. We connect the input to one NAND gate with an inverted selecting line, and another NAND gate with a non-inverted selecting line. At the final stage, we connect each result to an inverter NAND gate.
DMUX Verilog
module DMux( input in, input sel, output a, output b); wire w1,w2,w3; nand Nand1(w1,sel,sel); nand Nand2(w2,in,w1); nand Nand3(w3,in,sel); nand Nand4(a,w2,w2); nand Nand5(b,w3,w3); Endmodule

## Slide 35: 16-bit Variants
Basic gates with 16-bit input

## Slide 36: OR 16-bit Gate
We build OR16 by taking the 16-bit inputs through NOT gates and then pass their outputs through another NAND gate.
OR 16-bit HDL
CHIP Or16 { IN a[16], b[16]; OUT out[16]; PARTS: Or(a=a[0],b=b[0],out=out[0]); Or(a=a[1],b=b[1],out=out[1]); Or(a=a[2],b=b[2],out=out[2]); Or(a=a[3],b=b[3],out=out[3]); Or(a=a[4],b=b[4],out=out[4]); Or(a=a[5],b=b[5],out=out[5]); Or(a=a[6],b=b[6],out=out[6]); Or(a=a[7],b=b[7],out=out[7]); Or(a=a[8],b=b[8],out=out[8]); Or(a=a[9],b=b[9],out=out[9]); Or(a=a[10],b=b[10],out=out[10]); Or(a=a[11],b=b[11],out=out[11]); Or(a=a[12],b=b[12],out=out[12]); Or(a=a[13],b=b[13],out=out[13]); Or(a=a[14],b=b[14],out=out[14]); Or(a=a[15],b=b[15],out=out[15]); }

## Slide 37: OR 16-bit Gate
We build OR16 by taking the 16-bit inputs through NOT gates and then pass their outputs through another NAND gate.
OR 16-bit Verilog
module Or16( input [15:0] a, input [15:0] b, output [15:0] out ); or Or0(out[0],a[0],b[0]); or Or1(out[1],a[1],b[1]); or Or2(out[2],a[2],b[2]); or Or3(out[3],a[3],b[3]); or Or4(out[4],a[4],b[4]); or Or5(out[5],a[5],b[5]); or Or6(out[6],a[6],b[6]); or Or7(out[7],a[7],b[7]); or Or8(out[8],a[8],b[8]); or Or9(out[9],a[9],b[9]); or Or10(out[10],a[10],b[10]); or Or11(out[11],a[11],b[11]); or Or12(out[12],a[12],b[12]); or Or13(out[13],a[13],b[13]); or Or14(out[14],a[14],b[14]); or Or15(out[15],a[15],b[15]); Endmodule

## Slide 38: AND 16-bit Gate
We build a 16-bit AND gate by connecting the two inputs A and B to a NAND gate and then connecting the result to both inputs of the NAND gate.
AND 16-bit
CHIP And16 { IN a[16], b[16]; OUT out[16]; PARTS: And(a=a[0],b=b[0],out=out[0]); And(a=a[1],b=b[1],out=out[1]); And(a=a[2],b=b[2],out=out[2]); And(a=a[3],b=b[3],out=out[3]); And(a=a[4],b=b[4],out=out[4]); And(a=a[5],b=b[5],out=out[5]); And(a=a[6],b=b[6],out=out[6]); And(a=a[7],b=b[7],out=out[7]); And(a=a[8],b=b[8],out=out[8]); And(a=a[9],b=b[9],out=out[9]); And(a=a[10],b=b[10],out=out[10]); And(a=a[11],b=b[11],out=out[11]); And(a=a[12],b=b[12],out=out[12]); And(a=a[13],b=b[13],out=out[13]); And(a=a[14],b=b[14],out=out[14]); And(a=a[15],b=b[15],out=out[15]); }

## Slide 39: NOT 16-bit Gate
We build a 16-bit NOT gate by connecting both inputs of NAND gate to the input signal.
NOT 16-bit
CHIP Not16 { IN in[16]; OUT out[16]; PARTS: Not(in=in[0],out=out[0]); Not(in=in[1],out=out[1]); Not(in=in[2],out=out[2]); Not(in=in[3],out=out[3]); Not(in=in[4],out=out[4]); Not(in=in[5],out=out[5]); Not(in=in[6],out=out[6]); Not(in=in[7],out=out[7]); Not(in=in[8],out=out[8]); Not(in=in[9],out=out[9]); Not(in=in[10],out=out[10]); Not(in=in[11],out=out[11]); Not(in=in[12],out=out[12]); Not(in=in[13],out=out[13]); Not(in=in[14],out=out[14]); Not(in=in[15],out=out[15]); }

## Slide 40: MUX 16-bit Gate
MUX 16-bit HDL
CHIP Mux16 { IN a[16], b[16], sel; OUT out[16]; PARTS: Mux(a=a[0],b=b[0],sel=sel,out=out[0]); Mux(a=a[1],b=b[1],sel=sel,out=out[1]); Mux(a=a[2],b=b[2],sel=sel,out=out[2]); Mux(a=a[3],b=b[3],sel=sel,out=out[3]); Mux(a=a[4],b=b[4],sel=sel,out=out[4]); Mux(a=a[5],b=b[5],sel=sel,out=out[5]); Mux(a=a[6],b=b[6],sel=sel,out=out[6]); Mux(a=a[7],b=b[7],sel=sel,out=out[7]); Mux(a=a[8],b=b[8],sel=sel,out=out[8]); Mux(a=a[9],b=b[9],sel=sel,out=out[9]); Mux(a=a[10],b=b[10],sel=sel,out=out[10]); Mux(a=a[11],b=b[11],sel=sel,out=out[11]); Mux(a=a[12],b=b[12],sel=sel,out=out[12]); Mux(a=a[13],b=b[13],sel=sel,out=out[13]); Mux(a=a[14],b=b[14],sel=sel,out=out[14]); Mux(a=a[15],b=b[15],sel=sel,out=out[15]); }
We build a 16-bit MUX using 4 NAND gates. We connect A to an inverted selection line, and B to a non-inverted selection line, and then combine the results using another NAND gate.

## Slide 41: MUX 16-bit Gate
We build a 16-bit MUX using 4 NAND gates. We connect A to an inverted selection line, and B to a non-inverted selection line, and then combine the results using another NAND gate.
MUX 16-bit Verilog
module Mux16(input [15:0] a, input [15:0] b, input sel, output [15:0] out ); Mux m0(.a(a[0]),.b(b[0]),.sel(sel),.out(out[0])); Mux m1(.a(a[1]),.b(b[1]),.sel(sel),.out(out[1])); Mux m2(.a(a[2]),.b(b[2]),.sel(sel),.out(out[2])); Mux m3(.a(a[3]),.b(b[3]),.sel(sel),.out(out[3])); Mux m4(.a(a[4]),.b(b[4]),.sel(sel),.out(out[4])); Mux m5(.a(a[5]),.b(b[5]),.sel(sel),.out(out[5])); Mux m6(.a(a[6]),.b(b[6]),.sel(sel),.out(out[6])); Mux m7(.a(a[7]),.b(b[7]),.sel(sel),.out(out[7])); Mux m8(.a(a[8]),.b(b[8]),.sel(sel),.out(out[8])); Mux m9(.a(a[9]),.b(b[9]),.sel(sel),.out(out[9])); Mux m10(.a(a[10]),.b(b[10]),.sel(sel),.out(out[10])); Mux m11(.a(a[11]),.b(b[11]),.sel(sel),.out(out[11])); Mux m12(.a(a[12]),.b(b[12]),.sel(sel),.out(out[12])); Mux m13(.a(a[13]),.b(b[13]),.sel(sel),.out(out[13])); Mux m14(.a(a[14]),.b(b[14]),.sel(sel),.out(out[14])); Mux m15(.a(a[15]),.b(b[15]),.sel(sel),.out(out[15])); Endmodule

## Slide 42: Multi-way Variants
Basic gates with 16-bit input

## Slide 43: OR8Way Gate
We use 7 elementary OR gates to build OR8WAY. Each OR gate has 2 inputs, with 4 of them comparing the inputs and the other 3 comparing the outputs.
OR8Way
CHIP Or8Way { IN in[8]; OUT out; PARTS: Or(a=in[0],b=in[1],out=w1); Or(a=in[2],b=in[3],out=w2); Or(a=in[4],b=in[5],out=w3); Or(a=in[6],b=in[7],out=w4); Or(a=w1,b=w2,out=w5); Or(a=w3,b=w4,out=w6); Or(a=w5,b=w6,out=out); }

## Slide 44: MUX4WAY Gate
Mux4Way HDL
CHIP Mux4Way16 { IN a[16], b[16], c[16], d[16], sel[2]; OUT out[16]; PARTS: Mux16(a=a,b=b,sel=sel[0],out=w1); Mux16(a=c, b=d,sel=sel[0],out=w2); Mux16(a=w1,b=w2,sel=sel[1],out=out); }
We build MUX4WAY with 3 2:1 MUXs each MUX selects one of two inputs based on the selection line bit 0 and then selects one of the 2 results based on the selection line bit 1.

## Slide 45: MUX4WAY Gate
We build MUX4WAY with 3 2:1 MUXs each MUX selects one of two inputs based on the selection line bit 0 and then selects one of the 2 results based on the selection line bit 1.
Mux4Way Verilog
module Mux4Way16( input [15:0] a, input [15:0] b, input [15:0] c, input [15:0] d, input [1:0] sel, output [15:0] out ); wire [15:0] w1,w2; Mux16 m1(.a(a),.b(b),.sel(sel[0]),.out(w1)); Mux16 m2(.a(c),.b(d),.sel(sel[0]),.out(w2)); Mux16 m3(.a(w1),.b(w2),.sel(sel[1]),.out(out)); Endmodule

## Slide 46: MUX8WAY Gate
We build MUX8WAY with 7 2:1 MUXs each MUX selects one of two inputs based on the selection line bit 0 and then selects one of the 2 results based on the selection line bit 1 at the last stage it selects one of the results based on the selection line bit 3.
Mux8Way HDL
CHIP Mux8Way16 { IN a[16], b[16], c[16], d[16], e[16], f[16], g[16], h[16], sel[3]; OUT out[16]; PARTS: Mux16(a=a, b=b, sel=sel[0], out=w1); Mux16(a=c, b=d, sel=sel[0], out=w2); Mux16(a=w1, b=w2, sel=sel[1], out=w3); Mux16(a=e, b=f, sel=sel[0], out=w4); Mux16(a=g, b=h, sel=sel[0], out=w5); Mux16(a=w4, b=w5, sel=sel[1], out=w6); Mux16(a=w3, b=w6, sel=sel[2], out=out); }

## Slide 47: MUX8WAY Gate
We build MUX8WAY with 7 2:1 MUXs each MUX selects one of two inputs based on the selection line bit 0 and then selects one of the 2 results based on the selection line bit 1 at the last stage it selects one of the results based on the selection line bit 3.
Mux8Way Verilog
module Mux8Way16( input [15:0] a, input [15:0] b, input [15:0] c, input [15:0] d, input [15:0] e, input [15:0] f, input [15:0] g, input [15:0] h, input [2:0] sel, output [15:0] out ); wire [15:0] w1,w2; Mux4Way16 m0(.a(a),.b(b),.c(c),.d(d),.sel(sel[1:0]),.out(w1)); Mux4Way16 m1(.a(e),.b(f),.c(g),.d(h),.sel(sel[1:0]),.out(w2)); Mux16 m2(.a(w1),.b(w2),.sel(sel[2]),.out(out)); Endmodule

## Slide 48: DMUX4WAY Gate
We build a DMUX4WAY with 3 2:1 DMUXs, where the input is split into two paths based on the selection line to display the input on one of the outputs.
DMux4Way HDL
CHIP DMux4Way { IN in, sel[2]; OUT a, b, c, d; PARTS: DMux(in=in,sel=sel[1],a=w1,b=w2); DMux(in=w1,sel=sel[0],a=a,b=b); DMux(in=w2,sel=sel[0],a=c,b=d); }

## Slide 49: DMUX4WAY Gate
We build a DMUX4WAY with 3 2:1 DMUXs, where the input is split into two paths based on the selection line to display the input on one of the outputs.
DMux4Way Verilog
module DMux4Way( input in, input [1:0] sel, output a, output b, output c, output d ); wire w1 ,w2; DMux Dm1(.in(in),.sel(sel[1]),.a(w1),.b(w2)); DMux Dm2(.in(w1),.sel(sel[0]),.a(a),.b(b)); DMux dm3(.in(w2),.sel(sel[0]),.a(c),.b(d)); Endmodule

## Slide 50: DMUX8WAY Gate
We build a DMUX8WAY with 7 2:1 DMUXs, where the input is split into two paths based on the selection line to display the input on one of the outputs.
DMux4Way HDL
CHIP DMux8Way { IN in, sel[3]; OUT a, b, c, d, e, f, g, h; PARTS: DMux(in=in,sel=sel[2],a=w1,b=w2); DMux(in=w1,sel=sel[1],a=w3,b=w4); DMux(in=w2,sel=sel[1],a=w5,b=w6); DMux(in=w3,sel=sel[0],a=a,b=b); DMux(in=w4,sel=sel[0],a=c,b=d); DMux(in=w5,sel=sel[0],a=e,b=f); DMux(in=w6,sel=sel[0],a=g,b=h); }

## Slide 51: DMUX8WAY Gate
We build a DMUX8WAY with 7 2:1 DMUXs, where the input is split into two paths based on the selection line to display the input on one of the outputs.
DMux8Way Verilog
module DMux8Way( input in, input [2:0] sel, output a, output b, output c, output d, output e, output f, output g, output h ); wire w1,w2,w3,w5,w4,w6; DMux dm1 (.in(in),.sel(sel[2]),.a(w1),.b(w2)); DMux dm2 (.in(w1),.sel(sel[1]),.a(w3),.b(w4)); DMux dm3 (.in(w2),.sel(sel[1]),.a(w5),.b(w6)); DMux dm4 (.in(w3),.sel(sel[0]),.a(a),.b(b)); DMux dm5 (.in(w4),.sel(sel[0]),.a(c),.b(d)); DMux dm6 (.in(w5),.sel(sel[0]),.a(e),.b(f)); DMux dm7 (.in(w6),.sel(sel[0]),.a(g),.b(h)); endmodule

## Slide 52: Personality type career
Design
Design the architecture
Phase 01
Hardware implementation
Phase 02
Software implementation
Phase 03
Game or application
Phase 04

## Slide 53: Thanks!
Do you have any questions?
youremail@freepik.com
+34 654 321 432
yourwebsite.com
Please keep this slide for attribution